## Slide 1: PWM Drawer
Utilizing the “tiny” for useful applications.

## Slide 2: Table of contents 01 04 02 05 03 06
Description
Features
Materials
Working Principle
Flow Chart
Schematic Diagram

## Slide 3: Description 01

## Slide 4: Description
The ATtiny84 PWM Wave Drawing Project utilizes the capabilities of the ATtiny84 microcontroller to visualize Pulse Width Modulation (PWM) waves generated by an external signal generator
on an LCD display. This innovative project offers an exploration of microcontroller interfacing
and signal processing using Timer 1 of the microcontroller. The ATtiny84, a compact yet
powerful microcontroller, interprets the incoming PWM signals and displays their
Frequencies and Duty cycles, then translates the input wave into a visual
representation. With this compact device, users can observe and
analyze the waveform characteristics.

## Slide 5: Features 02

## Slide 6: Features
The project can measure up to 100KHz
In the 100KHz range, it provides a 100% accuracy
Up to 4 significant figures in frequency measurement.
100KHz
100%
4

## Slide 7: Materials 03

## Slide 8: Materials
ATtiny84
16*2 LCD Screen
20MHz Crystal Oscillator

## Slide 9: Working Principle 04

## Slide 10: Working Principle
The main principle of operation is using the input capture unit (ICU) of ATtiny84’s Timer 1 to measure the frequency and duty cycle using the following steps:
The ICU captures the time between 3 consecutive edges of the input PWM wave (2 rising, 1 falling).
The frequency is calculated getting the reciprocal of the time difference between the 1st and 3rd captures (Period).
The duty cycle is calculated by dividing the time difference between 1st and 2nd captures by the Period.

## Slide 11: Flow Chart 05

## Slide 12: Flow Chart:

## Slide 13: Schematic Diagram 06

## Slide 14: Schematic Diagram

## Slide 15: Thanks
Made by: Belal Hassan
Email: Bilal.1021023@stemegypt.edu.eg
Phone Number: +20 120 439 7890
Please keep this slide for attribution